## Slide 1: 基於RTAB-MAP的 室外自動導航系統的實現
組別：A90
組員名單：許晏誠、何立平、張瀚
指導教授：邱偉育 prof.

## Slide 2
許晏誠
107061126
電機系
何立平
107000206
電資班
張瀚
107061130
電機系

## Slide 3: How Autonomous Navigation works?
Cognition of the Environment
Motion Planning & Control
Path planning
Obstacle avoidance
SLAM
Global Planner
(Costmap)
Local Planner
(Costmap)
Local Planner
& Hardware controller

## Slide 4: Autonomous System Flow (Exploration & Pre-Built Mode)
Location & Poses
Obstacle location
Input Image
SLAM
Sensor
Feature Extraction
Loop Closure Detection
Odometry
Mapping
Feature point
(Pointcloud)
Local
costmap
Global
costmap
Static map
Local
planner
Global
planner
Navigation
Arduino
(Hardware)
Pointcloud & Laser Scan
Static map
Global
path
trajectory
(movement instruction)

## Slide 5: 硬體架構 光達 深度攝影機 車體：阿克曼轉向架構
相機
光達
阿卡漫架構
The model of our hardware system is based on a four-wheel drive RC remote car.
Four-wheel driving and a large storage area enabled us to lay our laptop which works
as the computing core, on the car. Sensors are set up according to the tf including a
RGB-D camera which can also perform as a stereo camera and a 2D lidar which allows
the robot to detect the obstacle 360. Fig. 10 shows our robot model containing a Lidar
on top and stereo camera at the front.

## Slide 6: 深度攝影機 位置 功能   避開前方的障礙物   環境3D地圖的建立   車體座標的定位
相機
The D435i works as the “eye” of the
robot which enables it to see the obstacle at front and
provide the image data for RTAB-MAP to build the
map and compute the odometry

## Slide 7: 光達 (lidar) 位置 功能   可以避開360°的障礙物   優化「即時定位、地圖構建」的效果

## Slide 8: 阿克曼轉向架構 (ackermann steering geometry) 介紹   透過前輪的轉向來轉彎   用於一般轎車 選用此架構的原因   車體較大、車體穩定   較符合實際自駕車的架構 前輪 後輪
This model is commonly used in ordinary cars, so it’s also called a car-like model. We
chose this steering system because car-like models are the most common one on the
road. Once the system for ackerman is integrated, there’d be no need to put extra effort
on developing differential models. Second, a stable but large enough model to meet our
purpose is hard to find, so we’d prefer the Ackerman model as our choice. The
following Fig. 9 shows how Ackerman steering geometry works.

## Slide 9: SLAM (Real-Time Appearance-Based Mapping - RTABMAP)
Sensor
Feature Extraction
Loop Closure Detection
Odometry
Mapping
Input Image
Feature point
(Pointcloud)
Location & Poses
Ref Labbé, Mathieu, and François Michaud. "RTAB‐Map as an open‐source lidar and visual simultaneous localization and mapping library for large‐scale and long‐term online operation." Journal of Field Robotics 36.2 (2019): 416-446.

## Slide 10: Navigation (TEB_LOCAL_PLANNER)
Ref: https://pojenlai.wordpress.com/2015/07/16/ros-navigation-stack-%E7%B0%A1%E4%BB%8B/
Teb Local Planner
Recovery Behavior

## Slide 11: Result & Analysis (Mapping)
Precise Mapping with following concern:
Auto-Exposure ROI, Sensor position adjustment
Odometry drift or False obstacle -> Remapping
Mapping speed cannot be too fast -> Time Consuming

## Slide 12: Result & Analysis (Navigation & Obstacle avoidance)
Point to Point Navigation -> Suffer from odometry drifting
Obstacle Avoidance -> Fast objects are unavoidable
Detection of in-sight object -> Restricted range of detection